## Slide 1
01
Proposed Solution
A MALE UAV loiters for 20+ hours beyond line of sight. Nobody can hear the engine. We give the ground station a physics twin that flies alongside the real engine and reports the difference.
STEP 1
Model the engine
A mean value engine model runs in step with the real one, from the same throttle and altitude.
STEP 2
Subtract, don't threshold
Each channel becomes a residual: measured minus physics-expected, in sigma.
STEP 3
Two-stage diagnosis
An autoencoder gates anomalies; a multi-task network names the fault and its severity.
STEP 4
Answer, with evidence
Fault, confidence, remaining life, the driving channel, and the action to take.
The insight that makes it work
A raw exhaust temperature of 740 °C means nothing on its own. It is normal at sea level at full power and alarming at 25,000 ft in a descent. A fixed threshold must therefore be set loose enough to avoid false alarms, which makes it slow. By subtracting what the physics model expects under those exact conditions, the residual is near zero whenever the engine is healthy, at every altitude and power setting. A fault becomes visible as a departure from zero rather than a crossing of a fixed line.
Capability | What the operator gets
Health monitoring | 15 residual channels at 20 Hz, per cylinder
Fault prediction | 9 fault modes named, with severity and confidence
Sensor integrity | A failed probe is separated from a failed cylinder
Mission reliability | Remaining useful life and a recommended action
Any powerplant | 10 engines shipped; an operator can define their own
EngineTwin · SIH 2026 · PS 26054 · DRDO · AI-Enabled Real-Time Digital Twin for Aero Piston Engines in MALE UAVs
1

## Slide 2
02
Technical Approach
Five models in one pipeline. The physics layer is what lets the learned layers stay small, fast and explainable enough to run on flight hardware.
Stage | Model | What it does | Why this choice
Plant | Mean Value Engine Model | Manifold filling, turbo boost and altitude derating, crankshaft torque balance, per-cylinder thermal states, oil circuit | Gives an expected value for every channel under the current condition
Estimation | Physics-anchored Kalman estimator, 12 states | Fuses measurement with the physics prediction; coasts on physics alone if the datalink drops | Linear, so no Jacobian: the non-linear dynamics are already integrated by the plant
Gate | Undercomplete autoencoder | Reconstructs the healthy residual vector; a high reconstruction error flags an anomaly | Trained only on healthy data, so it generalises to faults it has never seen
Diagnosis | Multi-task classifier, temperature-scaled | Names the fault class, estimates severity, flags sensor-versus-engine | Scaling makes the confidence figure honest rather than overconfident
Prognosis | Regime-aware RUL estimator | Projects health trend to a limit; reports an interval, not a point | Classifies drift as stable, drifting or abrupt before extrapolating
Explanation | Gradient x input attribution | Ranks which residual channels drove this decision | Exact and costs one backward pass, unlike sampling-based methods
Implementation
Python, FastAPI and WebSocket streaming at 20 Hz, PyTorch for the learned layers, Three.js for the 3D twin. Fully offline: no external service, no CDN, no API key.
Data flow
Engine simulation to telemetry to residuals to diagnosis to frontend state to the 3D model. The visualisation reads the same frame the AI reads, and holds no engine values of its own.
EngineTwin · SIH 2026 · PS 26054 · DRDO · AI-Enabled Real-Time Digital Twin for Aero Piston Engines in MALE UAVs
2

## Slide 3
03
Feasibility, Challenges and Risk
The hard part of this problem is not accuracy on a test set. It is not crying wolf at 25,000 ft, and fitting inside a flight computer's budget.
Feasibility
Constraint | Requirement | Measured
Inference budget | 50 ms at 20 Hz | 0.403 ms
Compute | Embedded flight SBC | Single CPU thread
Connectivity | Beyond line of sight | Runs fully offline
Retraining | Per airframe | Config-driven, no code change
Challenges met
False alarms at altitude.
A fixed threshold misfires as air density falls. Residuals removed the altitude dependence: the false alarm rate above 20,000 ft fell from 18.42 % to 0.70 %.
A broken probe is not a broken engine.
A dedicated validator cross-checks thermodynamic consistency, so a dead thermocouple is reported as a sensor fault instead of aborting a healthy sortie.
Risks and mitigation
Risk | Mitigation
Models trained on one engine may not transfer | Physics is re-parameterised per engine; diagnosis is reported as uncalibrated on any other, never silently trusted
Simulated training data may not match a real engine | Build-variant sampling and sensor noise modelling; the residual definition is what transfers, not the weights
A confident wrong answer is worse than none | Temperature scaling calibrates confidence; the autoencoder gate must fire before the classifier is believed
Operator cannot audit an AI decision | Every alert carries the ranked channels that drove it, and the physics value it departed from
EngineTwin · SIH 2026 · PS 26054 · DRDO · AI-Enabled Real-Time Digital Twin for Aero Piston Engines in MALE UAVs
3

## Slide 4
04
Impact and Benefits
Benchmarked against the two things this would actually replace: a conventional threshold-based engine instrument system, and a black-box model on raw telemetry.
Metric | Fixed-threshold EIS | Black-box ML on raw telemetry | EngineTwin
Classification accuracy | 53.65 % | 86.93 % | 97.64 %
Macro F1 score | 0.2463 | 0.8696 | 0.9769
Mean detection latency | 28.26 s | 8.00 s | 2.87 s
False alarm rate, healthy engine | 0.00 % | 11.74 % | 1.41 %
Sensor fault vs engine fault | No, false abort | No, confounded | Yes, physics-decoupled
Explanation of a decision | None | Feature importance only | Ranked evidence per alert
Remaining useful life | None | None | Interval, with regime
Where the gain comes from
An ablation isolates it. Swapping physics residuals for raw telemetry, with the same network and the same training budget, drops macro F1 from 0.9762 to 0.9165 and raises the false alarm rate from 0.47 % to 14.78 %. The physics layer, not the network, is what earns the result.
Operational benefit
Detection 25 seconds earlier than an EIS is the difference between a diverted sortie and a lost airframe. A 1.41 % false alarm rate is low enough that crews act on the alarm rather than learn to ignore it, which is the failure mode that retires most monitoring systems.
EngineTwin · SIH 2026 · PS 26054 · DRDO · AI-Enabled Real-Time Digital Twin for Aero Piston Engines in MALE UAVs
4

## Slide 5
05
Research and References
The methods this work builds on, and an honest statement of what our engine data is and is not.
Methods
Source | Used for
Heywood, Internal Combustion Engine Fundamentals, McGraw-Hill | Combustion, friction and thermal sub-models
Hendricks and Sorenson, Mean Value Modelling of Spark Ignition Engines, SAE 1990 | The mean value engine model structure
Gagg and Farrar altitude power relation | Naturally aspirated power lapse with density
ICAO Standard Atmosphere | Density, pressure and temperature with altitude
Sakurada and Yairi, Anomaly Detection Using Autoencoders, MLSDA 2014 | Healthy-only autoencoder as the anomaly gate
Guo et al., On Calibration of Modern Neural Networks, ICML 2017 | Temperature scaling so confidence is honest
Shrikumar et al., Learning Important Features Through Propagating Activation Differences, ICML 2017 | Gradient x input attribution
Engine data provenance
Category | Basis
Displacement, cylinders, layout, rated power and speed, compression ratio | Manufacturer published specification
Naturally aspirated altitude power curve | Computed from the Gagg-Farrar relation against ISA density
Operating limits, sensor characteristics, turbocharged power curve | Modelled to be internally consistent with the rated point
Every engine config in the repository carries this classification per field, so a reviewer can see which figures are transcribed and which are modelled without having to ask.
Reproducibility
Every number on slide 4 is printed by validation/benchmark.py and validation/ablation.py in this repository, against a held-out test set. Both can be re-run from a clean checkout to reproduce the table.
EngineTwin · SIH 2026 · PS 26054 · DRDO · AI-Enabled Real-Time Digital Twin for Aero Piston Engines in MALE UAVs
5